## Slide 1
Measuring & Marking Tools.
Lecturer: James Rix

## Slide 2
Aims & Objectives.
Aims:
Objectives:
Identify types of measuring and marking tools.
Identify Measuring & Marking Tools 1
Identify Measuring & Marking Tools 2
Identify Measuring & Marking Tools 3
Identify Measuring & Marking Tools 4
Identify Measuring & Marking Tools 5
Identify Measuring & Marking Tools 6

## Slide 3
Measuring & Marking Tools
1.

## Slide 4
Measuring & Marking Tools 1.
Tape Measure
Boat Level
Steel Rule
Pencil
Scribe
Spirit Level

## Slide 5
Measuring & Marking Tools 1:
Pencil.
9H
8H
7H
6H
5H
4H
3H
2H
H
F
HB
B
2B
3B
4B
5B
6B
7B
8B
9B
Rubber
Lead
Wood Casing
Ferule
A pencil is a drawing and writing instrument that comes in many grades (see bottom of slide). The lead is a graphite powder mixed with a clay binder that creates a mark from physical abrasion.
Pencils are mainly used for drawing and sketching and in this case for marking wood for cutting or shaping. As well as different shades pencils come in colours too.

## Slide 6
Measuring & Marking Tools 1:
Scribe.
Head
Body
A scribe is used for marking wood accurately. Sometimes preferred over a pencil or instead of a pencil. Scribes produce fine markings that reduce the need for aftercare or removal. A basic scribe is a steel spike with a tip sharpened to a fine point.

## Slide 7
Measuring & Marking Tools 1:
Tape Measure.
A tape measure is a tool used for measuring. It has linear measurement markings and can be found in both metric and imperial versions. Most tape measures have both metric and imperial measurement markings.
Tape measures can typically be bought in 3m, 5m and 8m lengths.
Tape measures consist of a metal strip that retracts into the body/case of the tape measure.
Thumb Lock
Body/Case
Belt Loop
Blade
Hook
Spring & Stop
8m
5m
3m
1
1
2
3
Imperial
Metric

## Slide 8
Measuring & Marking Tools 1:
Steel Rule.
1
1
2
3
Imperial
Metric
Rule Blade
Steel rules are an essential part of the toolkit. A metal blade with measurements marked along the edges. Usually has both imperial and metric measurements. Steel rules come in various lengths; the more popular lengths are 150mm/6” and 305mm/12”. Steel rules are more accurate than folding rules as they are rigid and made in one piece.
150mm/6”
300mm/12”

## Slide 9
Measuring & Marking Tools 1:
Spirit Level.
90o
180o
45o
Level Vials
Box Beam Construction
A spirit level is a tool used to check work for level (horizontal) or plumb (Vertical). Some levels also have a 3rd vial for 45o angles. The vials are a yellowish-green colour with additives for UV protection. The best spirit level is accurate to within 0.5mm. Spirit levels are also known as bubble levels or simply level.
Plumb
Level
Check for level here
Check for plumb here

## Slide 10
Measuring & Marking Tools 1:
Boat Level.
90o
180o
45o
Level Vials
A spirit level is a tool used to check work for level (horizontal) or plumb (Vertical). Some levels also have a 3rd vial for 45o angles. The vials are a yellowish-green colour with additives for UV protection. The best spirit level is accurate to within 0.5mm. Spirit levels are also known as bubble levels or simply a level.
Plumb
Level
Check for level here
Check for plumb here

## Slide 11
Measuring & Marking Tools
2.

## Slide 12
Measuring & Marking Tools 2.
Digital Calipers
Inside Calipers
Dividers
Outside Calipers

## Slide 13
Measuring & Marking Tools 2:
Digital Calipers.
Main scale
Depth Rod
LCD Display
Lower jaws for outside measurement
Upper jaws for inside measurement
Digital calipers are the next generation of Vernier calipers. With a digital readout and ability to switch between metric and imperial measurements. Used for measuring distances either internally or externally. Digital calipers are extremely accurate. Powered by a small battery.

## Slide 14
Measuring & Marking Tools 2:
Inside Calipers.
An instrument used to measure the inside distance of a gap. For example, when turning a bowl, inside calipers would be used to determine the internal size of the object.
Legs
Centering Collar
Spring Loaded Tension Knob
Spring
Internal measurement

## Slide 15
Measuring & Marking Tools 2:
Outside Calipers.
External measurement
Legs
Centering Collar
Spring Loaded Tension Knob
Spring
An instrument used to measure the outside distance of a gap. For example, when turning a spindle, outside calipers would be used to determine the external size of the object.

## Slide 16
Measuring & Marking Tools 2:
Dividers.
Often referred to as a compass the dividers main use is for marking out arcs and circles and for dividing up a measurement into equal increments. The divider has 2 points, one on each arm. One is for pivoting on and the other is for the marking. The distance between each leg is adjusted at the centering collar using the spring-loaded tension knob and once set can repeat the same measurement over and over.
Legs
Centering Collar
Spring Loaded Tension Knob
Spring
Equal parts

## Slide 17
Measuring & Marking Tools
3.

## Slide 18
Measuring & Marking Tools 3.
Chalk Line and Reel
Marking Knife
Straight Edge
Trammel heads

## Slide 19
Measuring & Marking Tools 3:
Chalk Line & Reel.
Chalk
Reel
Chalk pen
Hook and line
Crank
Door
Box
A chalk line is a tool used to mark out straight lines. It is used mainly on a flat surface over distances that can't be achieved by rulers or straightedges. The line is charged with chalk while in the reel, the line is then stretched between the two points and twanged against the surface producing a straight line. When marking a plumb line the reel itself can be used as a weight to stretch the line.

## Slide 20
Measuring & Marking Tools 3:
Marking Knife.
Single bevel blade
Pins
Hardwood handle
High carbon steel
Left-handed
Right-handed
A marking knife is a tool used for scribing markings onto wood. Used in place of a pencil or scribe. Marking knives are comprised of a steel blade encases in a handle with a single bevel blade. The blade is sharpened on the left side for left-handed people and the right side for right-handed people.

## Slide 21
Measuring & Marking Tools 3:
Trammel Heads.
Pins
Thumbscrews
Trammel heads are a tool primarily used for marking arcs and circles. They are also known as Trammel Points or trammels. They are clamped to a straight and true beam of either wood or metal and are only restricted by the length of said beam. The trammel pins or points can be replaced with a pencil creating a bigger scale compass.
Clamps

## Slide 22
Measuring & Marking Tools 3:
Straight Edge.
Various Lengths
A straight edge also spelt straightedge is used for marking straight lines or checking for straightness. Straight edges are used in many different trades including those outside of construction. They comprise of steel or aluminum lengths of square and true bars. A pair of straight edges can be used as winding sticks to check for twists.
Steel or aluminum blade
Using 2 straight edges for winding stick

## Slide 23
Measuring & Marking Tools
4.

## Slide 24
Measuring & Marking Tools 4.
Try Square
Mitre Square
Combination Square
Sliding Bevel

## Slide 25
Measuring & Marking Tools 4:
Try Square.
A try square is used for marking and checking square. In marking it allows a 90o angle to be produced off a straight edge. In checking it allows you to check stock for squareness on all sides and ends. The try square is composed of two main parts - the stock and the blade.
Blade
Stock
Rivets
Wear Plate
90o

## Slide 26
Measuring & Marking Tools 4:
Mitre Square.
Blade
Stock
Rivets
Wear Plate
45o
A mitre square is used for marking and checking mitres/45o. In marking it allows a 45o angle to be produced off a straight edge. In checking it allows you to check stock for mitres. The mitre square is composed of two main parts - the stock and the blade.

## Slide 27
Measuring & Marking Tools 4:
Combination Square.
45o
90o
Blade
Stock
Level
Scribe
Mitre
Square
A combination square is a tool used for marking out 90o and 45o lines in woodworking, stonemasonry and metalworking. It also has a level and scribe functions. Combination squares can have interchangeable heads to give it more functions hence the name combination square, it has a combination of uses.

## Slide 28
Measuring & Marking Tools 4:
Sliding Bevel.
A sliding bevel is an adjustable marking tool used in carpentry and joinery for transferring and setting angles. It consists of a stock and a movable blade that can be locked in place with a screw or lever. Because the blade pivots freely, the sliding bevel is ideal for copying existing angles, marking dovetails or mitres, and checking accuracy during layout work. It’s a versatile tool that helps ensure consistent, repeatable angles across a project.
Blade
Tightening Screw
Stock

## Slide 29
Measuring & Marking Tools
5.

## Slide 30
Measuring & Marking Tools 5.
Marking Gauge
Cutting Gauge
Combination Gauge
Mortice Gauge

## Slide 31
Measuring & Marking Tools 4:
Marking Gauge.
Tightening Screw
Stock/Fence
Beam
Fixed Pin
A marking gauge is a precision tool used in carpentry and joinery to scribe parallel lines along a piece of timber. It consists of a stem, a fence (or stock), and a sharp pin or cutter that marks the surface. By adjusting the fence, the marking gauge ensures consistent measurements from the edge, making it ideal for tasks like marking out joints, rebates, or tenons with accuracy and repeatability.

## Slide 32
Measuring & Marking Tools 4:
Mortice Gauge.
Tightening Screw
Fixed Pin
Moveable Pin
Beam
Stock/Fence
A mortice gauge is a marking tool used in carpentry and joinery to scribe two parallel lines at a set distance, usually for marking out mortices and tenons. It looks similar to a marking gauge but has two adjustable pins instead of one, allowing precise marking of both sides of a joint. The fence slides along the stem and locks in place, ensuring consistent spacing and accuracy when laying out work.

## Slide 33
Measuring & Marking Tools 4:
Combination Gauge.
Tightening Screw
Second Pin Adjustment
Beam
Stock/Fence
Moveable Pin
Marking Gauge Side.
Mortice Gauge Side.
Fixed Pin
Fixed Pin
A combination gauge is a versatile marking tool used in carpentry and joinery that combines the functions of both a marking gauge and a mortice gauge. It has a single pin on one side for marking parallel lines and a pair of adjustable pins on the other for marking mortices. With its sliding stock and dual‑purpose design, the combination gauge allows quick switching between tasks, making it especially useful for efficient, accurate layout work.

## Slide 34
Measuring & Marking Tools 4:
Cutting Gauge.
Tightening Screw
Beam
Stock/Fence
Blade
A cutting gauge is a marking tool used in carpentry and joinery to score clean, accurate lines across the grain. Instead of a pin, it uses a small blade that slices the fibres, helping prevent tear‑out and giving a sharper, more precise mark. It’s especially useful when marking shoulders, rebates, or any layout where a crisp, clean line is essential for accuracy.

## Slide 35
Measuring & Marking Tools
6.

## Slide 36
Measuring & Marking Tools 6.
Folding Rule
Profile Gauge
Dovetail Square 1:8
Builders Square
Dovetail Square 1:6
Speed Square

## Slide 37
Measuring & Marking Tools 6:
Folding Rule.
A folding rule is a traditional measuring tool used in carpentry and joinery for taking accurate linear measurements. Made from wood or plastic, it consists of several hinged sections that fold together for easy storage and unfold to form a straight ruler. Unlike a tape measure, it stays rigid when extended, making it ideal for marking straight lines and measuring internal spaces with precision.

## Slide 38
Measuring & Marking Tools 6:
Dovetail Square 1:6.
0
0
1
1
2
3
4
5
6
A 1:6 dovetail square is a specialist marking tool used in fine carpentry and joinery to set out dovetail joints with consistent accuracy. The 1:6 ratio gives a gentle slope ideal for softwoods, helping create strong, clean‑fitting dovetails. Its fixed angle allows the user to mark both the tail and pin sides quickly and repeatably, ensuring each joint is uniform and precise.
Stock
Blade

## Slide 39
Measuring & Marking Tools 6:
Dovetail Square 1:8.
0
0
1
1
2
3
4
5
6
7
8
A 1:8 dovetail square is a fixed‑angle marking tool used to lay out dovetail joints with a steeper, more refined slope suited to hardwoods. The 1:8 ratio creates a stronger mechanical lock in dense timber, helping the joint resist pulling forces. Its precise, unchanging angle allows carpenters and joiners to mark tails and pins quickly and consistently, ensuring clean, accurate dovetail layouts every time.
Stock
Blade

## Slide 40
Measuring & Marking Tools 6:
Builders Square.
Tongue
Body
A builder’s square is a large, L‑shaped measuring tool used in carpentry and joinery to check and mark accurate 90‑degree angles on timber and sheet materials. Its long, rigid arms make it ideal for squaring door frames, stud walls, and larger construction layouts where precision over distance matters. Durable and easy to read, the builder’s square helps ensure structures stay true, straight, and properly aligned.

## Slide 41
Measuring & Marking Tools 6:
Profile Gauge.
A profile gauge, also known as a contour gauge, is a handy marking tool used in carpentry and joinery to copy the exact shape of an irregular surface. It consists of a row of sliding pins that move independently, allowing the gauge to press against mouldings, pipes, trims, or other uneven profiles and capture their outline. This shape can then be transferred directly onto timber for accurate cutting and fitting, making the profile gauge ideal for scribing work and precision finishing.

## Slide 42
Measuring & Marking Tools 6:
Speed Square.
Right Angle
T Edge
Angles
45o
45o
Line Guide
Hip/Valley
Commons
Pivot Point
A speed square is a triangular measuring tool used in carpentry and joinery for marking and checking angles quickly. Made from metal or plastic, it combines the
functions of a try square,
protractor, and saw guide. Its 90° and 45° edges make it ideal for marking perpendicular or mitre cuts, while the degree scale allows for precise angle layout. It’s a compact, versatile tool that helps ensure accuracy and efficiency in everyday marking tasks.

## Slide 43
Recap.
Identified Measuring & Marking Tools 1
Identified Measuring & Marking Tools 2
Identified Measuring & Marking Tools 3
Identified Measuring & Marking Tools 4
Identified Measuring & Marking Tools 5
Identified Measuring & Marking Tools 6
In this session we…

## Slide 44
Any Questions?
If you have any questions why not try and look up the answer online using a search engine and typing in your question, if you cant find your answer then ask your tutor or email them your questions at:
Lecturer@college.ac.uk

## Slide 45
Thank You.
We would like to take this opportunity to thank you for using this material. If you have any questions or suggestion on this or any other learning material produced by Educon please email:
Educon.rix@gmail.com
Lecturer: James Rix