## Slide 1
6219 - L1 Ext Certificate Construction Skills/Carpentry & Joinery.
Unit 005: Constructing Half Brick Walling.
Lecturer: James Rix
Half Brick Walling.

## Slide 2
Aim & Objectives.
Aim:
Objectives:
Know how to set out and build brick walls
1.1 identify the Personal Protective Equipment (PPE) appropriate to building half brick thick walls
1.2 identify the materials required to build half brick thick walls
1.3 identify the tools and equipment required to build half brick thick walls
1.4 state the number of bricks required to build a 1m2 brick walls.

## Slide 3
PPE

## Slide 4
Activities.
Activity:
Brief:
005.1a – Gear Up & Get Safe!
This activity introduces learners to the essential Personal Protective Equipment (PPE) required when constructing half‑brick thick walls.

## Slide 5
Types of Personal Protective Equipment (PPE).
Options:
A range of helmets, hard hats and bump caps
Hazards:
Impact from falling or flying objects, risk of head bumping, hair entanglement
Note:
Some safety helmets incorporate or can be fitted with specially-designed eye or hearing protection. Don’t forget neck protection, eg scarves for use during welding. Do not use head protection if it is damaged – replace it.
Hard Hat

## Slide 6
Types of Personal Protective Equipment (PPE).
Options:
Conventional or disposable overalls, boiler suits, specialist protective clothing, eg chain-mail aprons, high-visibility clothing
Hazards:
Temperature extremes, adverse weather, chemical or metal splash, spray from pressure leaks or spray guns, impact or penetration, contaminated dust, excessive wear or entanglement of own clothing.
Note:
The choice of materials includes flame-retardant, anti-static, chain mail, chemically impermeable, and high-visibility. Don’t forget other protection, like safety harnesses or life jackets.
Hi Vis Vest/Jacket

## Slide 7
Types of Personal Protective Equipment (PPE).
Options:
Safety boots and shoes with protective toe caps and penetration-resistant mid-sole, gaiters, leggings, spats.
Hazards:
Wet, electrostatic build-up, slipping, cuts and punctures, falling objects, metal and chemical splash, abrasion.
Note: Footwear can have a variety of sole patterns and materials to help prevent slips in different conditions, including oil or chemical-resistant soles. It can also be anti-static, electrically conductive or thermally insulating. It is important that the appropriate footwear is selected for the risks identified
Safety Boots/Shoes

## Slide 8
Types of Personal Protective Equipment (PPE).
Options:
Safety spectacles, goggles, face-shields, visors
Hazards:
Chemical or metal splash, dust, projectiles, gas and vapour, radiation
Note:
Make sure the eye protection has the right combination of impact/dust/ splash/molten metal eye protection for the task and fits the user properly.
Safety Specs/Goggles

## Slide 9
Types of Personal Protective Equipment (PPE).
Options:
Gloves, gauntlets, mitts, wrist-cuffs, armlets
Hazards:
Abrasion, temperature extremes, cuts and punctures, impact, chemicals, electric shock, skin infection, disease or contamination.
Note:
Avoid gloves when operating machines such as bench drills where the gloves could get caught. Some materials are quickly penetrated by chemicals so be careful when you are selecting them, see HSE’s skin at work website (www.hse.gov.uk/skin).
Safety Gloves

## Slide 10
Types of Personal Protective Equipment (PPE).
Options:
Barrier Cream
Hazards:
skin infection, disease or contamination
Note:
Barrier creams are unreliable and are no substitute for proper PPE
Barrier Cream

## Slide 11
Types of Personal Protective Equipment (PPE).
Options:
Disposable filtering face-piece or respirator
Hazards:
Dust
Note:
The right type of respirator filter must be used as each is effective for only a limited range of substances.
Dust Mask

## Slide 12
Types of Personal Protective Equipment (PPE).
Options:
half- or full-face respirators, airfed helmets, breathing apparatus.
Hazards:
Dust, vapour, gas, oxygen-deficient atmospheres
Note:
The right type of respirator filter must be used as each is effective for only a limited range of substances. Where there is a shortage of oxygen or any danger of losing consciousness due to exposure to high levels of harmful fumes, only use breathing apparatus – never use a filtering cartridge. Filters only have a limited life; when replacing them or any other part, check with the manufacturer’s guidance and ensure the correct replacement part is used
Respirator

## Slide 13
Types of Personal Protective Equipment (PPE).
Options:
Foam earplugs, wax balls, ear defenders, Silicon Plugs, Universal Earplugs, otoplasties
Hazards:
Damage to hearing, hearing loss, deafness
Note:
Should be used when noise level is 80 db or more. It is important that the correct type of ear protection is used for the noise level you are working in. This type of PPE is not covered under Personal Protective Equipment At Work Regulations 1992/2002 as it has its own regulation. The Control of Noise at Work Regulations 2005
Ear Defenders

## Slide 14
Types of Personal Protective Equipment (PPE).
Options:
Conventional or disposable overalls, boiler suits, specialist protective clothing, eg chain-mail aprons
Hazards:
Temperature extremes, adverse weather, chemical or metal splash, spray from pressure leaks or spray guns, impact or penetration, contaminated dust, excessive wear or entanglement of own clothing.
Note:
The choice of materials includes flame-retardant, anti-static, chain mail, chemically impermeable, and high-visibility. Don’t forget other protection, like safety harnesses or life jackets
Overalls

## Slide 15
Types of Personal Protective Equipment (PPE).
Options:
Harness
Hazards:
Falling from height
Note:
This is not covered under the Personal protection Equipment At Work 1992/2002, it has its own regulation. Working at Height regulations 2005
Harness

## Slide 16
Conformite Europeenne.
CE Marking.
It is extremely important when buying PPE that you make sure
that this symbol is displayed on the item being bought. This marking
is covered under the European Directive 89/686/EEC and ensures that the quality of the PPE is of acceptable standards. Always buy CE marked PPE.
European Economic Area

## Slide 17
Materials

## Slide 18
Activities.
Activity:
Brief:
005.1.2: Build It Right.
This activity introduces learners to the core materials used when constructing half‑brick thick walls. Learners will explore the differences between common bricks, facing bricks, and mortar, and understand how each contributes to the structure, strength, and appearance of brickwork.

## Slide 19
Bricks.
Engineering Brick
Common Brick
Facing Brick

## Slide 20
Brick Size.
215mm
102.5mm
65mm

## Slide 21
Brick Parts.
Stretcher
Header
Arris
Frog

## Slide 22
Brick Bats.
Quarter
Bat
Half Bat
3 Quarter
Bat

## Slide 23
Brick Closers.
King
Closer
Beveled
Closer
Queen
Closer

## Slide 24
Brick Bonds.
Stretcher
Contains full and half bat bricks. Course 1 is a series of full bricks with the second course beginning with a half bat followed by full bricks

## Slide 25
Brick Bonds.
Header
Contains full bricks and half bats and 3 quarter bats. Course 1 is a full brick followed by a series of half bats; second course is a 3-quarter bat followed by half bats.

## Slide 26
Brick Bonds.
Flemish
Contains full, 1 quarter and 3 quarter bats. First course contains a full brick followed by a half bat, alternated. The second course starts with 1 quarter bat, then half bat then full brick

## Slide 27
Brick Bonds.
English
Contains full, 1 quarter and 3 quarter bats. First course is series of full bricks, second course starts with 1 quarter bat then a series of half bats.

## Slide 28
Pointing Styles
Weather Struck
Recessed
Bucket Handle
Flush

## Slide 29
Blocks.
Dense
Block
Lightweight
Block

## Slide 30
Mortar.
Builders sand is a finer grade sand than sharp sand. It has smaller particles and is used mainly with water and cement to make mortar for laying bricks, patio slabs and blocks.
Builders Sand
Cement
Cement is what’s known as a binder. It sets and hardens and adheres to other materials to bind them together.

## Slide 31
Mortar.
Hydrated Lime
Water
Hydrated lime otherwise known as calcium hydroxide is a white powder. It increases the workability of cement mortar. Hydrated lime is a non-hydraulic lime which harden when drying out. Hydraulic lime sets due to a chemical reaction.
Water or H2O is odorless, transparent, tasteless substance which covers 71% of the earths surface. It is vital to humanity but is also used in many things including construction.

## Slide 32
Mortar.
Plasticiser
Plasticiser is an additive used to increase the plasticity or decrease the viscosity of a material.

## Slide 33
Tools & Equipment

## Slide 34
Activities.
Activity:
Brief:
005.1.3: Tool Master.
This activity introduces learners to the core materials used when constructing half‑brick thick walls. Learners will explore the differences between common bricks, facing bricks, and mortar, and understand how each contributes to the structure, strength, and appearance of brickwork.

## Slide 35
Tape measures sold in the UK often have dual scales for metric and imperial units. Like the American tape measures described above, they also have markings every 16 in (40.6 cm) and 19.2 in (48.8 cm).
Tape Measure
Tools.

## Slide 36
A specialist tape measure designed to aid professional bricklayers in their work. The unique blade design accurately calculates brick and block quantities and course heights, plus there is a conventional metric scale, which is accurate to EC Class I, for general measuring.
Brick Measure
Tools.

## Slide 37
This will be the most expensive part of
the tool kit, thus keeping the bricklayers
work level (horizontal) and plumb
(vertical). These also come in various sizes. The main size for everyday work is nine hundred
millimeters or twelve hundred millimeters.
Spirit Level
Tools.

## Slide 38
Like the Spirit Level above, it has two bubbles, (one for levelling, the other for plumbing) but is smaller. It is very handy for decorative panels and soldier courses.
Boat Level
Tools.

## Slide 39
These came various sizes and shape ranging
between ten and fourteen inches. One side of the
trowel has a more rounded edge, this being for rough
cutting, however, this use is not advised for the
beginner. The measurements are the actual blade
size, the width of trowel also varies and beginners
will find a narrower trowel easier to use. The rounded
side on the trowel makes it suitable for both left and
right-handed operators. When the trowel is not in use for a period, clean it off dry and
apply a light coat of oil to avoid rusting.
Brick Trowel
Tools.

## Slide 40
Bucket trowels are a wide-bladed tool for scooping mortar from a bucket; it is also good for buttering bricks and smoothing mortar.
Bucket Trowel
Tools.

## Slide 41
These are used when corners of the building have to be built to run in the bricks between. The pins are tapered at the ends to allow for inserting into joints. It is important that the line is kept free of knots and clean of mortar.
Line & Pins
Tools.

## Slide 42
These are used in pairs as an easy method of holding the line up. These are inexpensive as you can make your own.
Line Blocks
Tools.

## Slide 43
Used with either a bolster or chisel. It is essential that the head is secure and checked regularly to ensure it never comes loose. Always wear eye protection goggles
Lump Hammer
Tools.

## Slide 44
Used for cutting bricks. Eye protection must be used at all times it is used. The end should never be allowed to burr over. This is known as a mushroom and can splinter when being hit. The end should be kept free from mushrooms by a grinding wheel which also allows the culling edge to be kept sharp.
Bolster Chisel
Tools.

## Slide 45
Similar to a bolster but with a smaller blade, used more for cutting into brickwork after it has been laid e.g. for letting in services. Again maintenance and safely procedures should be followed the same as for the bolster.
Cold Chisel
Tools.

## Slide 46
A Brick Hammer, also known as a Stonemasons Hammer, has one flat traditional face and a short or long chisel-shaped blade. It can thus be used to chip off edges or small pieces of stone, cut brick or a concrete masonry unit, without using a separate chisel. The chisel blade can also be used to rapidly cut bricks or cinder blocks. This type of hammer is also used by geologists when collecting rock and mineral samples and is one of several types of Geologist's hammer.
Brick Hammer
Tools.

## Slide 47
Scutch hammers have either one or two grooves for holding a scutch comb or drove in exactly the same way as a scutch chisel. Some scutch hammers have two grooves, one on each end of the head. These are known as 'double-ended scutch hammers’.
Scutch hammers, in conjunction with combs and droves, are used for cutting bricks in the same way as scutch chisels, however they are not as precise in their work, due to lack of control when wielding a hammer in comparison to a chisel. This is because the hammer needs more force to wield it than a chisel which needs a hammer/mallet to function.
Scutch Hammer
Tools.

## Slide 48
Used for putting a finish to the joints in brick work. A half-round joint which is also known as a bucket handle finish. Two types are shown, these can now be bought from shops, but an old pail or bucket handle can be bent to a suitable shape.
Jointer
Tools.

## Slide 49
A small hawk is used when pointing a lot and makes it easier to hold the mortar.
Hawk
Tools.

## Slide 50
This is used for setting out the work area and marking and checking right angles.
Builders Square
Tools.

## Slide 51
Inexpensive as you make it yourself. A length of timber with the vertical spacing of the bricks marked along one edge. Used when working from both ends of a wall to ensure that the courses are equal
Brick Gauge
Tools.

## Slide 52
A spade is a tool primarily for digging, comprising a blade – typically stunted and less curved than that of a shovel – and a long handle. Early spades were made of riven wood or of animal bones (often shoulder blades).
Spade
Tools.

## Slide 53
Supersedes the brick hod (original brick carrier). Used for carrying bricks around the work area.
Brick Carrier
Equipment.

## Slide 54
A spot is a dedicated place for mortar to be temporary placed while the bricklayer lays the bricks and builds the wall.
Spot
Equipment.

## Slide 55
Hand brush is a very useful piece of kit for brushing up, cleaning down. Bricklayers will use this type of brush for cleaning down their walls.
Hand Brush
Equipment.

## Slide 56
Floor brush used for cleaning down and brushing up.
Soft Floor Brush
Equipment.

## Slide 57
Another less expansive tool but of great use. II is used for holding the line up over long lengths of walling to remove any sagging
Tingle Plate
Equipment.

## Slide 58
Wheelbarrows are used to transport larger amounts of materials to the work area. Sometimes mortar is mixed in a wheelbarrow.
Wheelbarrow
Equipment.

## Slide 59
How many?

## Slide 60
Brick Size.
215mm
102mm
65mm
Brick Size.
Length: (stretcher) 215mm
Width: (header) 102mm
Height: 65mm

## Slide 61
How Many?
Work out how many bricks would be needed for a wall 3 courses high and 1 meter long.
1 meter long
3 courses high
Remember to add in the 10mm mortar gap in between bricks
Wall

## Slide 62
Mortar Ingredients.
Builders sand is a finer grade sand than sharp sand. It has smaller particles and is used mainly with water and cement to make mortar for laying bricks, patio slabs and blocks.
Cement is what’s known as a binder. It sets and hardens and adheres to other materials to bind them together.
Builders Sand
Cement

## Slide 63
Mortar Ingredients.
Hydrated Lime
Water
Hydrated lime otherwise known as calcium hydroxide is a white powder. It increases the workability of cement mortar. Hydrated lime is a non-hydraulic lime which harden when drying out. Hydraulic lime sets due to a chemical reaction.
Water or H2O is odorless, transparent, tasteless substance which covers 71% of the earths surface. It is vital to humanity but is also used in many things including construction.

## Slide 64
Mortar Ratios.
Mortar type | Minimum Compressive Strength | Cement: Sand: hydrates lime ratio | Uses
Type M | 2.500 psi | 3:12:1 | Underground, foundations, retaining walls, driveways
Type S | 1,800 psi | 2:9:1 | Underground, foundations, retaining walls, manholes, sewer walls, brick patios, pavements, and walkways
Type N | 750 psi | 1:6:1 | Above ground, general purpose, interior, exterior, mild load-bearing, chimneys, soft-stone or low-fired brick masonry
Type O | 350 psi | 1:9:2 | Above ground, non-load-bearing, interior
It is important that when mixing mortar that you mix the correct quantities throughout the project, otherwise you run the risk of having different shades of mortar and inconsistencies in strength across the structure.

## Slide 65
Calculating Mortar.
Each brick requires the following amounts for the mortar:
0.84kg Cement
1.7kg Sand
0.4ml Plasticiser
This is equal to 2lb of mortar per brick
All you need to do is multiply those amounts by the number of bricks in the wall.

## Slide 66
Group Activity.
Mr. Jones is a local man who wants a wall building but he only wants the wall to be 375mm high.
Mr. Jones asks, “how many courses of brick would be needed to get a wall 375mm high?”
65mm
10mm
If a brick is 65mm and the mortar gap is 10 mm that’s a total of 75mm all we have to do to find out how many courses are needed is to divide the height of the wall by the height of a brick and mortar.
375 divided by 75 = 5 courses

## Slide 67
Activities.
Activity:
Brief:
005.1.4: Let’s Build It!.
Learners will explore brick quantities for different wall thicknesses and practise calculating brick requirements.

## Slide 68
Recap.
In todays session we…
Identified PPE appropriate to building half brick walls
Identified the materials required to build half brick walls
Identified tools and equipment used to build half brick walls
Stated the number of bricks to build a 1m2 brick wall
Do you agree?

## Slide 69
Any Questions?
If you have any questions why not try and look up the answer online using a search engine and typing in your question, if you can't find your answer then ask your tutor or email them your questions at:
lecturer@college.ac.uk

## Slide 70
Personal Protective Equipment At Work Regulation 1992.pdf
https://www.youtube.com/watch?v=q2yAHDkC6Nw
https://www.youtube.com/watch?v=GRQ0iDq5UfM
https://www.youtube.com/watch?v=XVNMj0ZxZsI
Personal Protective Equipment at Work - A Brief Guide.pdf
OSHA - Personal Protective Equipment.pdf
http://www.hse.gov.uk/toolbox/ppe.htm
https://en.wikipedia.org/wiki/Personal_protective_equipment
Resources.

## Slide 71
Thank You.
We would like to take this opportunity to thank you for using this material. If you have any questions or suggestion on this or any other learning material produced by Educon please email:
educon.rix@gmail.com